## Slide 1: Challenge 1 - Psychophysics Prototype
Ioannis Georgopoulos & Sophia Silva
Setup addressed
#1, Visual vs. Auditory Reaction Time
Tools used
Arduino + Grove base shield
Push button, LED, buzzer, wires
Arduino IDE
StandardFirmata
Processing

## Slide 2: Wiring and Arduino
Wiring
Button: Digital port 2 (D2) → GND (internal pull-up, pressed = HIGH in this configuration)
LED: Digital port 4 (D4) → 220 ohm → LED anode, cathode → GND
Buzzer: Digital port 6 (D6) → buzzer (+), buzzer (-) → GND (passive buzzer via PWM)
Pin modes
Button, pin 2: input with pull-up
LED, pin 4: digital output
Buzzer, pin 6: PWM output
We uploaded StandardFirmata once; the board only reports its pins to the laptop.
All the logic (trial order, random wait, timing) runs in Processing.
On the Arduino

## Slide 3: Switching to Processing
Ioannis Georgopoulos & Sophia Silva
Talking to the Arduino
The Firmata library did not connect for us, so we send the Firmata commands ourselves with Serial.write.
LED: switched on and off with the digital-pin command.
Buzzer: PWM value 127 (50% duty) to sound it, 0 to stop it.
Button: serialEvent() saves System.nanoTime() the moment a press arrives.
Running the experiment
20 visual and 20 auditory trials, in random order.
Random wait of 1–4 s, then the LED or buzzer turns on. Reaction time = press time − stimulus time.
If press before the stimulus = false start
If no press within 2s = trial is invalid (subject was too slow).
Results are saved as a CSV, with the median and mean for each stimulus.